## Slide 1
Relay 1
Red
Blue Zone 2
Tstat
Green
White
Zone 1 A/C
Green
Zone 1 Heat White
Common 24v White
Zone 2 24V Hot
Zone 2 Heat
Zone 2 Fan (Y)
Zone 2 A/C
Honeywell Zone Switch
NC
NC
NC
NO
NO
NO
This relay array allows the Honeywell Zone Control to prioritize Zone 1, the first floor.
1. If there is no call for A/C from Zone 1, the first floor, Relay 1 in the normally closed state allows the A/C and Fan function from Zone 2, the basement, to be activated.
2. If Zone 1 is calling for A/C, Relay 1 is energized and Zone 2 A/C and Fan functions are disabled.
3. If there is no call for Heat from Zone 1, the first floor, Relay 2 in the normally closed state allows the Heat function from Zone 2, the basement, to be activated.
4. If Zone 1 is calling for Heat, Relay 2 is energized and Zone 2 Heat function is disabled.
Relay 2